## Slide 1: PRELIMINARY Well Spacing Calculations for the Trinity Aquifer, Kimble County Groundwater Conservation District January 20, 2025
Alyson McDonald, Ph.D., P.G.
Senior Hydrologist
Collier Consulting

## Slide 2: Outline
Edwards-Trinity Aquifer
Groundwater Availability Model (GAM)
Approach to well spacing
Hydraulic Properties
Water well data
Drawdown calculations
Well spacing recommendations

## Slide 3
Edwards Trinity Plateau Aquifer
(modified from Barker and Ardis, 1996) from Conceptual model report

## Slide 5
Edwards Trinity Plateau Groundwater Availability Model (EDDT GAM)
400 columns
300 rows
120,000 cells (1 mi x 1mi)
Layer 1: Edwards
Layer 2: Trinity
Notes: 300 cells by 400 cells
Rows columns
Layers - aquifers

## Slide 6: Proposed Process
  Step 1: Extract hydraulic property data (K, B, Ss and Sy) for EDDT GAM Layers 1 (Edwards) and 2 (Trinity) and calculate Transmissivity & Storativity
  Step 2: Evaluate available well data (Texas Water Development Board) and select well capacities (gpm)
  Step 3: Calculate distance drawdown for well capacities for a duration of 50 years (DFC planning)
  Step 4: Recommend well spacing for selected well capacities

## Slide 7: Actual Process
  Step 1: Extracted hydraulic property data (K, B, Ss and Sy) from EDDT GAM
    Calculated layer thickness and delineated zones for each aquifer
    Evaluated control points (field measurements) of hydraulic properties
    Consulted conceptual model report for hydraulic conductivity, specific yield, and specific storage values
    Assigned revised hydraulic conductivity, specific yield, and specific storage values to each zone
    Downloaded recent water level measurements for wells in Kimble County, calculated available drawdown
    Computed saturated thickness (bottom depth of the aquifer minus depth to water)
    Calculated transmissivity for each zone (saturated thickness x hydraulic conductivity)

## Slide 8: Actual Process, cont’d.
  Step 2: Evaluate available well data (Texas Water Development Board) and select well capacities (gpm)
  Step 3: Calculate distance drawdown for well capacities for a duration of 50 years (DFC planning)
  Step 4: Recommend well spacing for selected well capacities

## Slide 9: Aquifer Properties
  Thickness (B) – top to bottom (ft)
  Specific Storage, Specific Yield (Ss, Sy) – volume of water released per surface area when head is lowered (unitless)
  Hydraulic Conductivity (K) – rate that water moves through the aquifer under a hydraulic gradient (ft per day)
  Transmissivity (T) – Rate or volume that water moves through the thickness of the aquifer (ft2 per day). It is the product of saturated thickness and hydraulic conductivity.

## Slide 10: Edwards Aquifer

## Slide 11
Edwards Thickness (ft) GAM Layer 1
ZONE 1
ZONE 3
ZONE 2

## Slide 12: Storage (Sy) - Edwards

## Slide 13
Edwards Aquifer Specific Yield GAM calibrated
Specific Yield = 0.009 from EDDT GAM Conceptual Model Report

## Slide 14: Hydraulic Conductivity (Ksat) - Edwards

## Slide 15
Edwards Aquifer Ksat (ft per day) GAM Control Points

## Slide 16
Ksat Edwards Aquifer GAM Calibrated

## Slide 17: Saturated Thickness (B)- Edwards

## Slide 18
Edwards Aquifer Available Drawdown
Well Depth (ft) minus Depth to Water (ft)

## Slide 19
Edwards Aquifer Saturated Thickness Overlain on GAM Thickness
Saturated Thickness
ZONE 1: 50 ft
ZONE 2: 130 ft
ZONE 3: 220 ft

## Slide 20: Transmissivity (T) – Edwards saturated thickness x hydraulic conductivity
Calculated Transmissivity Edwards Layer 1 |  |  | 
Zone | Ksat (ft/day) | Saturated Thickness (ft) | Transmissivty (ft2 /day)
1 | 6.65 | 50 | 332.5
2 | 6.65 | 130 | 864.5
3 | 6.65 | 220 | 1463

## Slide 21
Edwards Transmissivity (ft2 per day) GAM Layer 1 and Calculated
Calculated Transmissivity Edwards Layer 1 |  |  | 
Zone | Ksat (ft/day) | Saturated Thickness (ft) | Transmissivty (ft2 /day)
1 | 6.65 | 50 | 332.5
2 | 6.65 | 130 | 864.5
3 | 6.65 | 220 | 1463
ZONE 1
ZONE 3
ZONE 2

## Slide 22: Well Yields – Kimble County

## Slide 23
Driller Reported Well Yields Edwards & Trinity

## Slide 24
TWDB Reported Well Yields Edwards

## Slide 25
Theis Distance Drawdown
Edwards Aquifer

## Slide 26
Chart: Drawdown at Distance from Pumping Well Edwards ZONE 1, 50 YEARS
| 1.8939393939393939E-4 | 9.46969696969697E-3 | 1.893939393939394E-2 | 3.787878787878788E-2 | 5.6818181818181816E-2 | 7.575757575757576E-2 | 9.4696969696969696E-2 | 0.18939393939393939 | 0.22727272727272727 | 0.28409090909090912 | 0.37878787878787878 | 0.47348484848484851 | 0.56818181818181823 | 0.66287878787878785 | 0.75757575757575757 | 0.85227272727272729 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42
17.36 gpm | 16.9062 | 10.6485 | 9.5398 | 8.4311 | 7.7825 | 7.3223 | 6.9654 | 5.8569 | 5.5654 | 5.2087 | 4.7491 | 4.3928 | 4.102 | 3.8563 | 3.6439 | 3.4567 | 3.2033 | 2.119 | 1.5104 | 1.1045 | 0.81466 | 0.60104 | 0.44146 | 0.32182 | 0.23235 | 0.16588 | 0.11697 | 0.081385 | 0.055831 | 0.03774 | 0.025123 | 0.016464 | 0.010617 | 0.0067359 | 0.0042038 | 0.002581 | 0.0015604 | 0.00093499 | 0.00058452 | 0.00051859 | 0.001138 | 0.0043464 | 0.017855 | 0.070901 | 0.26889 | 0.97504
30 gpm | 29.2157 | 18.4019 | 16.4858 | 14.5698 | 13.449 | 12.6538 | 12.037 | 10.1214 | 9.6176 | 9.0012 | 8.2069 | 7.5912 | 7.0886 | 6.6642 | 6.297 | 5.9736 | 5.5356 | 3.6619 | 2.6102 | 1.9088 | 1.4078 | 1.0387 | 0.76288 | 0.55613 | 0.40152 | 0.28666 | 0.20214 | 0.14064 | 0.096482 | 0.065218 | 0.043416 | 0.028451 | 0.018348 | 0.01164 | 0.0072646 | 0.0044602 | 0.0026965 | 0.0016158 | 0.0010101 | 0.00089619
50 gpm | 48.6928 | 30.6698 | 27.4764 | 24.283 | 22.415 | 21.0897 | 20.0617 | 16.869 | 16.0294 | 15.002 | 13.6782 | 12.652 | 11.8144 | 11.107 | 10.495 | 9.956 | 9.226 | 6.1031 | 4.3503 | 3.1813 | 2.3464 | 1.7311 | 1.2715 | 0.92689 | 0.66921 | 0.47777 | 0.33689 | 0.2344 | 0.1608 | 0.1087 | 0.07236 | 0.047419 | 0.030579 | 0.019401 | 0.012108 | 0.0074337 | 0.0044942 | 0.0026929 | 0.0016835 | 0.0014936
100 gpm | 97.3857 | 61.3395 | 54.9528 | 48.566 | 44.8301 | 42.1794 | 40.1235 | 33.738 | 32.0588 | 30.0041 | 27.3563 | 25.3041 | 23.6288 | 22.214 | 20.99 | 19.9119 | 18.452 | 12.2063 | 8.7006 | 6.3625 | 4.6927 | 3.4622 | 2.5429 | 1.8538 | 1.3384 | 0.95555 | 0.67379 | 0.46881 | 0.32161 | 0.21739 | 0.14472 | 0.094838 | 0.061159 | 0.038801 | 0.024215 | 0.014867 | 0.0089883 | 0.0053859 | 0.0033671 | 0.0029873
300 gpm | 292.157 | 184.0186 | 164.8583 | 145.698 | 134.4902 | 126.5383 | 120.3705 | 101.2139 | 96.1764 | 90.0122 | 82.0689 | 75.9122 | 70.8864 | 66.6419 | 62.9699 | 59.7358 | 55.3561 | 36.6189 | 26.1017 | 19.0876 | 14.0782 | 10.3866 | 7.6288 | 5.5613 | 4.0152 | 2.8666 | 2.0214 | 1.4064 | 0.96482 | 0.65218 | 0.43416 | 0.28451 | 0.18348 | 0.1164 | 0.072646 | 0.044602 | 0.026965 | 0.016158 | 0.010101 | 0.0089619

## Slide 27
Chart: Drawdown at Distance from Pumping Well Edwards ZONE 2, 50 YEARS
| 1.8939393939393939E-4 | 9.46969696969697E-3 | 1.893939393939394E-2 | 3.787878787878788E-2 | 5.6818181818181816E-2 | 7.575757575757576E-2 | 9.4696969696969696E-2 | 0.18939393939393939 | 0.22727272727272727 | 0.28409090909090912 | 0.37878787878787878 | 0.47348484848484851 | 0.56818181818181823 | 0.66287878787878785 | 0.75757575757575757 | 0.85227272727272729 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42
17.36 gpm | 6.7963 | 4.3895 | 3.9631 | 3.5366 | 3.2872 | 3.1102 | 2.9729 | 2.5465 | 2.4344 | 2.2971 | 2.1202 | 1.983 | 1.871 | 1.7763 | 1.6943 | 1.622 | 1.524 | 1.1012 | 0.8578 | 0.68916 | 0.56245 | 0.46295 | 0.38274 | 0.31702 | 0.26262 | 0.21732 | 0.17947 | 0.14781 | 0.12133 | 0.099218 | 0.080802 | 0.065511 | 0.052862 | 0.042443 | 0.033901 | 0.026933 | 0.021279 | 0.013056 | 0.010137 | 0.0078235 | 0.0060009 | 0.0045745 | 0.0034654 | 0.0026087 | 0.0019514 | 0.0014506 | 0.0010715 | 0.00078668 | 0.0005744 | 0.00041793 | 0.00030523 | 0.00022964 | 0.00019299 | 0.00021432
30 gpm | 11.7447 | 7.5856 | 6.8486 | 6.1117 | 5.6806 | 5.3748 | 5.1375 | 4.4007 | 4.2069 | 3.9697 | 3.664 | 3.4269 | 3.2332 | 3.0696 | 2.9279 | 2.803 | 2.6337 | 1.903 | 1.4824 | 1.1909 | 0.97198 | 0.80003 | 0.66142 | 0.54785 | 0.45384 | 0.37555 | 0.31014 | 0.25542 | 0.20967 | 0.17146 | 0.13964 | 0.11321 | 0.091351 | 0.073347 | 0.058585 | 0.046544 | 0.036773 | 0.022563 | 0.017518 | 0.01352 | 0.01037 | 0.0079053 | 0.0059887 | 0.0045082 | 0.0033723 | 0.0025067 | 0.0018517 | 0.0013595 | 0.00099262 | 0.00072222 | 0.00052746 | 0.00039684 | 0.00033351
50 gpm | 19.5746 | 12.6426 | 11.4144 | 10.1862 | 9.4677 | 8.958 | 8.5626 | 7.3344 | 7.0114 | 6.6161 | 6.1066 | 5.7115 | 5.3887 | 5.116 | 4.8799 | 4.6717 | 4.3894 | 3.1717 | 2.4706 | 1.9849 | 1.62 | 1.3334 | 1.1024 | 0.91308 | 0.7564 | 0.62592 | 0.5169 | 0.42571 | 0.34944 | 0.28577 | 0.23273 | 0.18868 | 0.15225 | 0.12224 | 0.097642 | 0.077573 | 0.061288 | 0.037605 | 0.029197 | 0.022533 | 0.017284 | 0.013176 | 0.0099811 | 0.0075137 | 0.0056205 | 0.0041779 | 0.0030861 | 0.0022658 | 0.0016544 | 0.0012037 | 0.00087911 | 0.00066139 | 0.00055585
100 gpm | 39.1492 | 25.2853 | 22.8288 | 20.3723 | 18.9354 | 17.9159 | 17.1251 | 14.6689 | 14.0228 | 13.2323 | 12.2132 | 11.4229 | 10.7775 | 10.232 | 9.7597 | 9.3434 | 8.7788 | 6.3434 | 4.9412 | 3.9698 | 3.2399 | 2.6668 | 2.2047 | 1.8262 | 1.5128 | 1.2518 | 1.0338 | 0.85141 | 0.69889 | 0.57153 | 0.46545 | 0.37737 | 0.3045 | 0.24449 | 0.19528 | 0.15515 | 0.12258 | 0.07521 | 0.058395 | 0.045066 | 0.034568 | 0.026351 | 0.019962 | 0.015027 | 0.011241 | 0.0083557 | 0.0061722 | 0.0045316 | 0.0033087 | 0.0024074 | 0.0017582 | 0.0013228 | 0.0011117
300 gpm | 117.4475 | 75.8558 | 68.4864 | 61.117 | 56.8063 | 53.7478 | 51.3754 | 44.0066 | 42.0685 | 39.6968 | 36.6395 | 34.2688 | 32.3325 | 30.6961 | 29.2792 | 28.0302 | 26.3365 | 19.0302 | 14.8237 | 11.9095 | 9.7198 | 8.0003 | 6.6142 | 5.4785 | 4.5384 | 3.7555 | 3.1014 | 2.5542 | 2.0967 | 1.7146 | 1.3964 | 1.1321 | 0.91351 | 0.73347 | 0.58585 | 0.46544 | 0.36773 | 0.22563 | 0.17518 | 0.1352 | 0.1037 | 0.079053 | 0.059887 | 0.045082 | 0.033723 | 0.025067 | 0.018517 | 0.013595 | 0.0099262 | 0.0072222 | 0.0052746 | 0.0039684 | 0.0033351

## Slide 28
Chart: Drawdown at Distance from Pumping Well Edwards ZONE 3, 50 YEARS
| 1.8939393939393939E-4 | 9.46969696969697E-3 | 1.893939393939394E-2 | 3.787878787878788E-2 | 5.6818181818181816E-2 | 7.575757575757576E-2 | 9.4696969696969696E-2 | 0.18939393939393939 | 0.22727272727272727 | 0.28409090909090912 | 0.37878787878787878 | 0.47348484848484851 | 0.56818181818181823 | 0.66287878787878785 | 0.75757575757575757 | 0.85227272727272729 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
17.36 gpm | 4.1116 | 2.6894 | 2.4374 | 2.1855 | 2.0381 | 1.9335 | 1.8524 | 1.6004 | 1.5341 | 1.453 | 1.3484 | 1.2673 | 1.2011 | 1.1451 | 1.0966 | 1.0539 | 0.99588 | 0.74517 | 0.59989 | 0.49825 | 0.42088 | 0.35913 | 0.30837 | 0.26583 | 0.22968 | 0.19869 | 0.17194 | 0.14875 | 0.12858 | 0.11102 | 0.095707 | 0.082359 | 0.070728 | 0.060603 | 0.051803 | 0.044166 | 0.037554 | 0.031841 | 0.026919 | 0.022688 | 0.019063 | 0.015966 | 0.013328 | 0.011089 | 0.0091949 | 0.0075979 | 0.0062564 | 0.0051334
30 gpm | 7.1053 | 4.6476 | 4.2122 | 3.7767 | 3.522 | 3.3413 | 3.2011 | 2.7656 | 2.6511 | 2.5109 | 2.3302 | 2.1901 | 2.0756 | 1.9789 | 1.8951 | 1.8212 | 1.721 | 1.2877 | 1.0367 | 0.86103 | 0.72732 | 0.62062 | 0.5329 | 0.45938 | 0.39692 | 0.34336 | 0.29713 | 0.25705 | 0.22221 | 0.19185 | 0.16539 | 0.14233 | 0.12223 | 0.10473 | 0.089521 | 0.076324 | 0.064898 | 0.055026 | 0.046519 | 0.039208 | 0.032943 | 0.027591 | 0.023032 | 0.019163 | 0.01589 | 0.01313 | 0.010812 | 0.0088711 | 0.0072526 | 0.005908 | 0.004795 | 0.0038773
50 gpm | 11.8422 | 7.7461 | 7.0203 | 6.2945 | 5.87 | 5.5688 | 5.3351 | 4.6094 | 4.4185 | 4.1849 | 3.8837 | 3.6502 | 3.4594 | 3.2982 | 3.1585 | 3.0354 | 2.8683 | 2.1462 | 1.7278 | 1.435 | 1.2122 | 1.0344 | 0.88817 | 0.76563 | 0.66153 | 0.57226 | 0.49522 | 0.42842 | 0.37034 | 0.31975 | 0.27565 | 0.23721 | 0.20371 | 0.17455 | 0.1492 | 0.12721 | 0.10816 | 0.091709 | 0.077531 | 0.065346 | 0.054905 | 0.045984 | 0.038387 | 0.031939 | 0.026483 | 0.021883 | 0.018019 | 0.014785 | 0.012088 | 0.0098466 | 0.0079917 | 0.0064622
100 gpm | 23.6844 | 15.4921 | 14.0406 | 12.5891 | 11.74 | 11.1375 | 10.6702 | 9.2188 | 8.837 | 8.3698 | 7.7675 | 7.3004 | 6.9188 | 6.5963 | 6.317 | 6.0707 | 5.7366 | 4.2925 | 3.4556 | 2.8701 | 2.4244 | 2.0687 | 1.7763 | 1.5313 | 1.3231 | 1.1445 | 0.99044 | 0.85684 | 0.74068 | 0.63951 | 0.55131 | 0.47442 | 0.40742 | 0.3491 | 0.2984 | 0.25441 | 0.21633 | 0.18342 | 0.15506 | 0.13069 | 0.10981 | 0.091969 | 0.076775 | 0.063877 | 0.052966 | 0.043767 | 0.036039 | 0.02957 | 0.024175 | 0.019693 | 0.015983 | 0.012924
300 gpm | 71.0533 | 46.4764 | 42.1218 | 37.7672 | 35.2199 | 33.4126 | 32.0107 | 27.6563 | 26.511 | 25.1093 | 23.3025 | 21.9012 | 20.7565 | 19.7889 | 18.951 | 18.2122 | 17.2099 | 12.8774 | 10.3667 | 8.6103 | 7.2732 | 6.2062 | 5.329 | 4.5938 | 3.9692 | 3.4336 | 2.9713 | 2.5705 | 2.2221 | 1.9185 | 1.6539 | 1.4233 | 1.2223 | 1.0473 | 0.89521 | 0.76324 | 0.64898 | 0.55026 | 0.46519 | 0.39208 | 0.32943 | 0.27591 | 0.23032 | 0.19163 | 0.1589 | 0.1313 | 0.10812 | 0.088711 | 0.072526 | 0.05908 | 0.04795 | 0.038773

## Slide 29
Zone 1 |  |  |  |  |  |  | Zone 2 |  |  |  |  |  |  | Zone 3 |  |  |  |  |  | 
gpm | 17.36 | 30 | 50 | 100 | 300 |  | gpm | 17.36 | 30 | 50 | 100 | 300 |  | gpm | 17.36 | 30 | 50 | 100 | 300 | 
r Dist. (ft) | S | S | S | S | S |  | r Dist. (ft) | S | S | S | S | S |  | r Dist. (ft) | S | S | S | S | S | 
1 | 16.9 | 29.2 | 48.7 | 97.4 | 292.2 |  | 1 | 6.8 | 11.7 | 19.6 | 39.1 | 117.4 |  | 1 | 4.1 | 7.1 | 11.8 | 23.7 | 71.1 | 
50 | 10.6 | 18.4 | 30.7 | 61.3 | 184.0 |  | 50 | 4.4 | 7.6 | 12.6 | 25.3 | 75.9 |  | 50 | 2.7 | 4.6 | 7.7 | 15.5 | 46.5 | 
100 | 9.5 | 16.5 | 27.5 | 55.0 | 164.9 |  | 100 | 4.0 | 6.8 | 11.4 | 22.8 | 68.5 |  | 100 | 2.4 | 4.2 | 7.0 | 14.0 | 42.1 | 
200 | 8.4 | 14.6 | 24.3 | 48.6 | 145.7 |  | 200 | 3.5 | 6.1 | 10.2 | 20.4 | 61.1 |  | 200 | 2.2 | 3.8 | 6.3 | 12.6 | 37.8 | 
300 | 7.8 | 13.4 | 22.4 | 44.8 | 134.5 |  | 300 | 3.3 | 5.7 | 9.5 | 18.9 | 56.8 |  | 300 | 2.0 | 3.5 | 5.9 | 11.7 | 35.2 | 
400 | 7.3 | 12.7 | 21.1 | 42.2 | 126.5 |  | 400 | 3.1 | 5.4 | 9.0 | 17.9 | 53.7 |  | 400 | 1.9 | 3.3 | 5.6 | 11.1 | 33.4 | 
500 | 7.0 | 12.0 | 20.1 | 40.1 | 120.4 |  | 500 | 3.0 | 5.1 | 8.6 | 17.1 | 51.4 |  | 500 | 1.9 | 3.2 | 5.3 | 10.7 | 32.0 | 
1000 | 5.9 | 10.1 | 16.9 | 33.7 | 101.2 |  | 1000 | 2.5 | 4.4 | 7.3 | 14.7 | 44.0 |  | 1000 | 1.6 | 2.8 | 4.6 | 9.2 | 27.7 | 
1200 | 5.6 | 9.6 | 16.0 | 32.1 | 96.2 |  | 1200 | 2.4 | 4.2 | 7.0 | 14.0 | 42.1 |  | 1200 | 1.5 | 2.7 | 4.4 | 8.8 | 26.5 | 
1500 | 5.2 | 9.0 | 15.0 | 30.0 | 90.0 |  | 1500 | 2.3 | 4.0 | 6.6 | 13.2 | 39.7 |  | 1500 | 1.5 | 2.5 | 4.2 | 8.4 | 25.1 | 
2000 | 4.7 | 8.2 | 13.7 | 27.4 | 82.1 |  | 2000 | 2.1 | 3.7 | 6.1 | 12.2 | 36.6 |  | 2000 | 1.3 | 2.3 | 3.9 | 7.8 | 23.3 | 
2500 | 4.4 | 7.6 | 12.7 | 25.3 | 75.9 |  | 2500 | 2.0 | 3.4 | 5.7 | 11.4 | 34.3 |  | 2500 | 1.3 | 2.2 | 3.7 | 7.3 | 21.9 | 
3000 | 4.1 | 7.1 | 11.8 | 23.6 | 70.9 |  | 3000 | 1.9 | 3.2 | 5.4 | 10.8 | 32.3 |  | 3000 | 1.2 | 2.1 | 3.5 | 6.9 | 20.8 | 
3500 | 3.9 | 6.7 | 11.1 | 22.2 | 66.6 |  | 3500 | 1.8 | 3.1 | 5.1 | 10.2 | 30.7 |  | 3500 | 1.1 | 2.0 | 3.3 | 6.6 | 19.8 | 
4000 | 3.6 | 6.3 | 10.5 | 21.0 | 63.0 |  | 4000 | 1.7 | 2.9 | 4.9 | 9.8 | 29.3 |  | 4000 | 1.1 | 1.9 | 3.2 | 6.3 | 19.0 | 
4500 | 3.5 | 6.0 | 10.0 | 19.9 | 59.7 |  | 4500 | 1.6 | 2.8 | 4.7 | 9.3 | 28.0 |  | 4500 | 1.1 | 1.8 | 3.0 | 6.1 | 18.2 | 
5280 | 3.2 | 5.5 | 9.2 | 18.5 | 55.4 |  | 5280 | 1.5 | 2.6 | 4.4 | 8.8 | 26.3 |  | 5280 | 1.0 | 1.7 | 2.9 | 5.7 | 17.2 | 

## Slide 30
TWDB Reported Well Yields Edwards Zones

## Slide 31
Pumping Capacity of Well As Equipped (gpm) | Minimum Distance from Existing Water Well (ft)
ZONE 1 | 
Up to 17.36 gpm | 150
> 17.36 to 30 gpm | 150
> 30 gpm to 50 gpm | 150
> 50 gpm to 100 gpm | 1200
> 100 gpm to 300 gpm | na
> 300 gpm | na
ZONE 2 | 
Up to 17.36 gpm | 150
> 17.36 to 30 gpm | 150
> 30 gpm to 50 gpm | 150
> 50 gpm to 100 gpm | 500
> 100 gpm to 300 gpm | na
> 300 gpm | na
ZONE 3 | 
Up to 17.36 gpm | 150
> 17.36 to 30 gpm | 150
> 30 gpm to 50 gpm | 150
> 50 gpm to 100 gpm | 150
> 100 gpm to 300 gpm | 150
> 300 gpm | 150

## Slide 32: Trinity Aquifer

## Slide 33: Outline
Trinity Aquifer
Groundwater Availability Model (GAM)
Approach to well spacing
Hydraulic properties
Water well data
Drawdown calculations
Well spacing recommendations

## Slide 34
Edwards Trinity Plateau Aquifer

## Slide 36
Edwards Trinity Plateau Groundwater Availability Model (EDDT GAM)
400 columns
300 rows
120,000 cells (1 mi x 1mi)
Layer 1: Edwards
Layer 2: Trinity
Notes: 300 cells by 400 cells
Rows columns
Layers - aquifers

## Slide 38: Process
  Step 1: Extracted hydraulic property data (K, B, Ss and Sy) from EDDT GAM
    Calculated layer thickness and delineated zones for each aquifer
    Evaluated control points (field measurements) of hydraulic properties
    Consulted conceptual model report for hydraulic conductivity, specific yield, and specific storage values
    Assigned revised hydraulic conductivity, specific yield, and specific storage values to each zone
    Downloaded recent water level measurements for wells in Kimble County, calculated available drawdown
    Computed saturated thickness (bottom depth of the aquifer minus depth to water)
    Calculated transmissivity for each zone (saturated thickness x hydraulic conductivity)

## Slide 39: Process, cont’d.
  Step 2: Evaluate available well data (Texas Water Development Board) and select well capacities (gpm)
  Step 3: Calculate distance drawdown for well capacities for a duration of 50 years (DFC planning)
  Step 4: Recommend well spacing for selected well capacities

## Slide 40: Step 1. Aquifer Properties
  Thickness (B) – top to bottom (ft)
  Specific Storage, Specific Yield (Ss, Sy) – volume of water released per surface area of aquifer when head is lowered (unitless)
  Hydraulic Conductivity (K) – rate that water moves through the aquifer under a hydraulic gradient (ft per day)
  Transmissivity (T) – Rate or volume that water moves through the thickness of the aquifer (ft2 per day). It is the product of saturated thickness and hydraulic conductivity.

## Slide 42
Trinity Thickness (ft) GAM Layer 2
ZONE 1
ZONE 3
ZONE 2

## Slide 43: Storage (S) - Trinity

## Slide 44
Trinity Aquifer Calibrated Storativity GAM
Storativity = 0.0003
ZONE 1
ZONE 3
ZONE 2

## Slide 45: Hydraulic Conductivity (Ksat) - Trinity

## Slide 46
Trinity Aquifer Ksat (ft/day) GAM Control Points

## Slide 47
Ksat Trinity Aquifer Calibrated GAM
Notes: In the North Plateau region of the Trinity hydrostratigraphic unit, the median hydraulic
conductivity derived from all well data is 7.0 feet per day.
5 ft per day for ZONE 3, Ksat will likely decrease further downdip.
17.37 and 16.8 from control points

## Slide 48
Ksat Trinity Aquifer (2022 conceptual model report)
ZONE 1
ZONE 3
ZONE 2

## Slide 49: Saturated Thickness (B) – Trinity Bottom of Aquifer (ft) – Depth to Water (ft)

## Slide 50
Trinity Aquifer Calculated Saturated Thickness Overlain on GAM Thickness
Saturated Thickness
ZONE 1: 180 ft
ZONE 2: 275 ft
ZONE 3: 464 ft
ZONE 1
ZONE 3
ZONE 2
Notes: Bsat increases as move downdip; assume confined downdip portions of the aquifer are saturated.

## Slide 51: Transmissivity (T) – Trinity saturated thickness x hydraulic conductivity
Calculated Transmissivity Trinity Layer 2 |  |  | 
Zone | Ksat (ft/day) | Saturated Thickness (ft) | Transmissivty (ft2 /day)
1 | 7 | 180 | 1260
2 | 7 | 275 | 1925
3 | 5 | 464 | 2320

## Slide 52
Trinity Transmissivity (ft2 per day) GAM Layer 2
ZONE 1
ZONE 3
ZONE 2

## Slide 53
ZONE 1
ZONE 3
ZONE 2
Calculated Transmissivity Trinity Layer 2 |  |  | 
Zone | Ksat (ft/day) | Saturated Thickness (ft) | Transmissivty (ft2 /day)
1 | 7 | 180 | 1260
2 | 7 | 275 | 1925
3 | 5 | 464 | 2320
Calculated Trinity Transmissivity (ft2 per day)

## Slide 54
Driller Reported Well Yields Edwards & Trinity

## Slide 55
TWDB Reported Well Yields Trinity

## Slide 56
Theis Distance Drawdown
Trinity Aquifer

## Slide 57
Chart: Drawdown at Distance from Pumping Well Trinity ZONE 1, 50 YEARS
| 1.8939393939393939E-4 | 9.46969696969697E-3 | 1.893939393939394E-2 | 3.787878787878788E-2 | 5.6818181818181816E-2 | 7.575757575757576E-2 | 9.4696969696969696E-2 | 0.18939393939393939 | 0.22727272727272727 | 0.28409090909090912 | 0.37878787878787878 | 0.47348484848484851 | 0.56818181818181823 | 0.66287878787878785 | 0.75757575757575757 | 0.85227272727272729 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42
17.36 gpm | 5.4604 | 3.8091 | 3.5165 | 3.2239 | 3.0527 | 2.9313 | 2.8371 | 2.5445 | 2.4676 | 2.3734 | 2.2519 | 2.1577 | 2.0808 | 2.0157 | 1.9594 | 1.9096 | 1.8422 | 1.5496 | 1.3786 | 1.2573 | 1.1633 | 1.0865 | 1.0217 | 0.96562 | 0.91623 | 0.87212 | 0.83229 | 0.796 | 0.76268 | 0.73192 | 0.70335 | 0.67669 | 0.65173 | 0.62826 | 0.60614 | 0.58522 | 0.5654 | 0.54657 | 0.52865 | 0.51157 | 0.49525 | 0.47964 | 0.4647 | 0.45037 | 0.43661 | 0.42339 | 0.41067 | 0.39842 | 0.38662 | 0.37525 | 0.36426 | 0.35366 | 0.34341 | 0.33351 | 0.32393 | 0.31465 | 0.30567 | 0.29698
30 gpm | 9.4361 | 6.5825 | 6.0768 | 5.5712 | 5.2754 | 5.0656 | 4.9028 | 4.3972 | 4.2642 | 4.1014 | 3.8916 | 3.7288 | 3.5958 | 3.4834 | 3.386 | 3.3001 | 3.1835 | 2.678 | 2.3823 | 2.1727 | 2.0103 | 1.8776 | 1.7656 | 1.6687 | 1.5833 | 1.5071 | 1.4383 | 1.3756 | 1.318 | 1.2648 | 1.2155 | 1.1694 | 1.1263 | 1.0857 | 1.0475 | 1.0113 | 0.97707 | 0.94453 | 0.91357 | 0.88404
50 gpm | 15.7269 | 10.9708 | 10.1281 | 9.2854 | 8.7924 | 8.4427 | 8.1714 | 7.3287 | 7.107 | 6.8357 | 6.486 | 6.2147 | 5.993 | 5.8056 | 5.6433 | 5.5001 | 5.3058 | 4.4633 | 3.9706 | 3.6212 | 3.3504 | 3.1294 | 2.9427 | 2.7812 | 2.6389 | 2.5119 | 2.3971 | 2.2926 | 2.1967 | 2.1081 | 2.0258 | 1.949 | 1.8771 | 1.8095 | 1.7458 | 1.6855 | 1.6285 | 1.5742 | 1.5226 | 1.4734
100 gpm | 31.4537 | 21.9415 | 20.2561 | 18.5707 | 17.5848 | 16.8853 | 16.3427 | 14.6573 | 14.214 | 13.6715 | 12.972 | 12.4294 | 11.9861 | 11.6113 | 11.2866 | 11.0002 | 10.6116 | 8.9265 | 7.9412 | 7.2424 | 6.7008 | 6.2587 | 5.8854 | 5.5623 | 5.2778 | 5.0237 | 4.7943 | 4.5852 | 4.3933 | 4.2161 | 4.0515 | 3.898 | 3.7542 | 3.619 | 3.4916 | 3.3711 | 3.2569 | 3.1484 | 3.0452 | 2.9468
300 gpm | 94.3611 | 65.8246 | 60.7684 | 55.7122 | 52.7545 | 50.656 | 49.0282 | 43.972 | 42.6421 | 41.0144 | 38.9159 | 37.2882 | 35.9582 | 34.8338 | 33.8598 | 33.0007 | 31.8347 | 26.7795 | 23.8235 | 21.7273 | 20.1025 | 18.7762 | 17.6561 | 16.687 | 15.8334 | 15.0711 | 14.3828 | 13.7557 | 13.18 | 12.6483 | 12.1546 | 11.694 | 11.2625 | 10.8571 | 10.4747 | 10.1133 | 9.7707 | 9.4453 | 9.1357 | 8.8404

## Slide 58
Chart: Drawdown at Distance from Pumping Well Trinity ZONE 2, 50 YEARS
| 1.8939393939393939E-4 | 9.46969696969697E-3 | 1.893939393939394E-2 | 3.787878787878788E-2 | 5.6818181818181816E-2 | 7.575757575757576E-2 | 9.4696969696969696E-2 | 0.18939393939393939 | 0.22727272727272727 | 0.28409090909090912 | 0.37878787878787878 | 0.47348484848484851 | 0.56818181818181823 | 0.66287878787878785 | 0.75757575757575757 | 0.85227272727272729 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42
17.36 gpm | 3.6326 | 2.5517 | 2.3602 | 2.1687 | 2.0567 | 1.9772 | 1.9156 | 1.724 | 1.6737 | 1.612 | 1.5325 | 1.4709 | 1.4205 | 1.3779 | 1.341 | 1.3085 | 1.2643 | 1.0728 | 0.96086 | 0.88143 | 0.81985 | 0.76957 | 0.72708 | 0.69031 | 0.65791 | 0.62896 | 0.60279 | 0.57894 | 0.55703 | 0.53678 | 0.51795 | 0.50037 | 0.48389 | 0.46838 | 0.45375 | 0.43989 | 0.42675 | 0.40232 | 0.39095 | 0.38006 | 0.36964 | 0.35964 | 0.35003 | 0.34079 | 0.3319 | 0.32333 | 0.31506 | 0.30707 | 0.29936 | 0.2919 | 0.28468 | 0.27768 | 0.27091 | 0.26434 | 0.25796
30 gpm | 6.2775 | 4.4097 | 4.0787 | 3.7478 | 3.5542 | 3.4168 | 3.3103 | 2.9793 | 2.8923 | 2.7858 | 2.6484 | 2.5419 | 2.4548 | 2.3812 | 2.3175 | 2.2612 | 2.1849 | 1.854 | 1.6605 | 1.5232 | 1.4168 | 1.3299 | 1.2565 | 1.1929 | 1.1369 | 1.0869 | 1.0417 | 1.0005 | 0.96261 | 0.92761 | 0.89508 | 0.8647 | 0.83622 | 0.80942 | 0.78413 | 0.76018 | 0.73746 | 0.69526 | 0.6756 | 0.65679 | 0.63877 | 0.62149 | 0.60489 | 0.58893 | 0.57356 | 0.55874 | 0.54446 | 0.53066 | 0.51733 | 0.50443 | 0.49195 | 0.47987 | 0.46816 | 0.4568
50 gpm | 10.4626 | 7.3495 | 6.7979 | 6.2463 | 5.9237 | 5.6947 | 5.5172 | 4.9656 | 4.8205 | 4.6429 | 4.414 | 4.2364 | 4.0913 | 3.9687 | 3.8624 | 3.7687 | 3.6415 | 3.09 | 2.7674 | 2.5387 | 2.3613 | 2.2165 | 2.0941 | 1.9882 | 1.8949 | 1.8115 | 1.7362 | 1.6675 | 1.6044 | 1.546 | 1.4918 | 1.4412 | 1.3937 | 1.349 | 1.3069 | 1.267 | 1.2291 | 1.1588 | 1.126 | 1.0946 | 1.0646 | 1.0358 | 1.0082 | 0.98155 | 0.95593 | 0.93124 | 0.90743 | 0.88443 | 0.86221 | 0.84072 | 0.81992 | 0.79978 | 0.78026
100 gpm | 20.9251 | 14.699 | 13.5958 | 12.4926 | 11.8473 | 11.3895 | 11.0343 | 9.9312 | 9.641 | 9.2858 | 8.828 | 8.4729 | 8.1827 | 7.9374 | 7.7248 | 7.5374 | 7.283 | 6.18 | 5.5349 | 5.0774 | 4.7226 | 4.433 | 4.1883 | 3.9765 | 3.7898 | 3.623 | 3.4723 | 3.3349 | 3.2087 | 3.092 | 2.9836 | 2.8823 | 2.7874 | 2.6981 | 2.6138 | 2.5339 | 2.4582 | 2.3175 | 2.252 | 2.1893 | 2.1292 | 2.0716 | 2.0163 | 1.9631 | 1.9119 | 1.8625 | 1.8149 | 1.7689 | 1.7244 | 1.6814 | 1.6398 | 1.5996 | 1.5605
300 gpm | 62.7754 | 44.097 | 40.7875 | 37.4779 | 35.542 | 34.1684 | 33.103 | 29.7935 | 28.923 | 27.8575 | 26.484 | 25.4186 | 24.5481 | 23.8121 | 23.1745 | 22.6122 | 21.849 | 18.5399 | 16.6047 | 15.2321 | 14.1679 | 13.299 | 12.5648 | 11.9294 | 11.3694 | 10.869 | 10.4169 | 10.0048 | 9.6261 | 9.2761 | 8.9508 | 8.647 | 8.3622 | 8.0942 | 7.8413 | 7.6018 | 7.3746 | 6.9526 | 6.756 | 6.5679 | 6.3877 | 6.2149 | 6.0489 | 5.8893 | 5.7356 | 5.5874 | 5.4446 | 5.3066 | 5.1733 | 5.0443 | 4.9195 | 4.7987 | 4.6816

## Slide 59
Chart: Drawdown at Distance from Pumping Well Trinity ZONE 3, 50 YEARS
| 1.8939393939393939E-4 | 9.46969696969697E-3 | 1.893939393939394E-2 | 3.787878787878788E-2 | 5.6818181818181816E-2 | 7.575757575757576E-2 | 9.4696969696969696E-2 | 0.18939393939393939 | 0.22727272727272727 | 0.28409090909090912 | 0.37878787878787878 | 0.47348484848484851 | 0.56818181818181823 | 0.66287878787878785 | 0.75757575757575757 | 0.85227272727272729 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
17.36 gpm | 3.0355 | 2.1387 | 1.9798 | 1.8209 | 1.7279 | 1.662 | 1.6108 | 1.4519 | 1.4101 | 1.359 | 1.293 | 1.2418 | 1.2001 | 1.1647 | 1.1341 | 1.1071 | 1.0705 | 0.91157 | 0.81865 | 0.75273 | 0.70163 | 0.65989 | 0.62463 | 0.5941 | 0.56719 | 0.54315 | 0.52142 | 0.5016 | 0.48339 | 0.46655 | 0.4509 | 0.43628 | 0.42257 | 0.40966 | 0.39747 | 0.38593 | 0.37498 | 0.36455 | 0.35461 | 0.34512 | 0.33603 | 0.32733 | 0.31897 | 0.31094 | 0.30321 | 0.29576 | 0.28858 | 0.28165
30 gpm | 5.2457 | 3.6959 | 3.4213 | 3.1467 | 2.986 | 2.8721 | 2.7837 | 2.5091 | 2.4368 | 2.3484 | 2.2345 | 2.1461 | 2.0738 | 2.0128 | 1.9599 | 1.9132 | 1.8499 | 1.5753 | 1.4147 | 1.3008 | 1.2125 | 1.1404 | 1.0794 | 1.0267 | 0.98018 | 0.93862 | 0.90107 | 0.86682 | 0.83535 | 0.80626 | 0.7792 | 0.75394 | 0.73024 | 0.70794 | 0.68688 | 0.66693 | 0.648 | 0.62999 | 0.61281 | 0.5964 | 0.5807 | 0.56566 | 0.55121 | 0.53733 | 0.52398 | 0.51111 | 0.49871 | 0.48673 | 0.47516 | 0.46397 | 0.45314 | 0.44265
50 gpm | 8.7428 | 6.1598 | 5.7021 | 5.2445 | 4.9767 | 4.7868 | 4.6394 | 4.1818 | 4.0614 | 3.914 | 3.7241 | 3.5768 | 3.4564 | 3.3546 | 3.2664 | 3.1887 | 3.0831 | 2.6255 | 2.3578 | 2.168 | 2.0208 | 1.9006 | 1.799 | 1.7111 | 1.6336 | 1.5644 | 1.5018 | 1.4447 | 1.3923 | 1.3438 | 1.2987 | 1.2566 | 1.2171 | 1.1799 | 1.1448 | 1.1116 | 1.08 | 1.05 | 1.0214 | 0.994 | 0.96784 | 0.94276 | 0.91869 | 0.89556 | 0.8733 | 0.85185 | 0.83118 | 0.81121 | 0.79193 | 0.77328 | 0.75523 | 0.73775
100 gpm | 17.4857 | 12.3196 | 11.4043 | 10.4889 | 9.9535 | 9.5736 | 9.2789 | 8.3635 | 8.1228 | 7.8281 | 7.4482 | 7.1535 | 6.9127 | 6.7092 | 6.5329 | 6.3773 | 6.1662 | 5.251 | 4.7157 | 4.336 | 4.0416 | 3.8012 | 3.5981 | 3.4222 | 3.2673 | 3.1287 | 3.0036 | 2.8894 | 2.7845 | 2.6875 | 2.5973 | 2.5131 | 2.4341 | 2.3598 | 2.2896 | 2.2231 | 2.16 | 2.1 | 2.0427 | 1.988 | 1.9357 | 1.8855 | 1.8374 | 1.7911 | 1.7466 | 1.7037 | 1.6624 | 1.6224 | 1.5839 | 1.5466 | 1.5105 | 1.4755
300 gpm | 52.4571 | 36.9588 | 34.2128 | 31.4667 | 29.8604 | 28.7207 | 27.8366 | 25.0906 | 24.3683 | 23.4843 | 22.3446 | 21.4605 | 20.7382 | 20.1275 | 19.5986 | 19.1319 | 18.4987 | 15.7529 | 14.1471 | 13.0081 | 12.1249 | 11.4037 | 10.7943 | 10.2667 | 9.8018 | 9.3862 | 9.0107 | 8.6682 | 8.3535 | 8.0626 | 7.792 | 7.5394 | 7.3024 | 7.0794 | 6.8688 | 6.6693 | 6.48 | 6.2999 | 6.1281 | 5.964 | 5.807 | 5.6566 | 5.5121 | 5.3733 | 5.2398 | 5.1111 | 4.9871 | 4.8673 | 4.7516 | 4.6397 | 4.5314 | 4.4265

## Slide 60
Trinity Aquifer Available Drawdown
Well Depth (ft) minus Depth to Water (ft)

## Slide 61
Zone 1 |  |  |  |  |  |  | Zone 2 |  |  |  |  |  |  | Zone 3 |  |  |  |  |  | 
gpm | 17.36 | 30 | 50 | 100 | 300 |  | gpm | 17.36 | 30 | 50 | 100 | 300 |  | gpm | 17.36 | 30 | 50 | 100 | 300 | 
r Dist. (ft) | S | S | S | S | S |  | r Dist. (ft) | S | S | S | S | S |  | r Dist. (ft) | S | S | S | S | S | 
1 | 5.5 | 9.4 | 15.7 | 31.5 | 94.4 |  | 1 | 3.6 | 6.3 | 10.5 | 20.9 | 62.8 |  | 1 | 5.9 | 10.2 | 17.0 | 34.1 | 102.2 | 
50 | 3.8 | 6.6 | 11.0 | 21.9 | 65.8 |  | 50 | 2.6 | 4.4 | 7.3 | 14.7 | 44.1 |  | 50 | 4.1 | 7.1 | 11.9 | 23.7 | 71.2 | 
100 | 3.5 | 6.1 | 10.1 | 20.3 | 60.8 |  | 100 | 2.4 | 4.1 | 6.8 | 13.6 | 40.8 |  | 100 | 3.8 | 6.6 | 10.9 | 21.9 | 65.7 | 
200 | 3.2 | 5.6 | 9.3 | 18.6 | 55.7 |  | 200 | 2.2 | 3.7 | 6.2 | 12.5 | 37.5 |  | 200 | 3.5 | 6.0 | 10.0 | 20.1 | 60.2 | 
300 | 3.1 | 5.3 | 8.8 | 17.6 | 52.8 |  | 300 | 2.1 | 3.6 | 5.9 | 11.8 | 35.5 |  | 300 | 3.3 | 5.7 | 9.5 | 19.0 | 57.0 | 
400 | 2.9 | 5.1 | 8.4 | 16.9 | 50.7 |  | 400 | 2.0 | 3.4 | 5.7 | 11.4 | 34.2 |  | 400 | 3.2 | 5.5 | 9.1 | 18.2 | 54.7 | 
500 | 2.8 | 4.9 | 8.2 | 16.3 | 49.0 |  | 500 | 1.9 | 3.3 | 5.5 | 11.0 | 33.1 |  | 500 | 3.1 | 5.3 | 8.8 | 17.6 | 52.9 | 
1000 | 2.5 | 4.4 | 7.3 | 14.7 | 44.0 |  | 1000 | 1.7 | 3.0 | 5.0 | 9.9 | 29.8 |  | 1000 | 2.7 | 4.7 | 7.9 | 15.8 | 47.4 | 
1200 | 2.5 | 4.3 | 7.1 | 14.2 | 42.6 |  | 1200 | 1.7 | 2.9 | 4.8 | 9.6 | 28.9 |  | 1200 | 2.7 | 4.6 | 7.7 | 15.3 | 46.0 | 
1500 | 2.4 | 4.1 | 6.8 | 13.7 | 41.0 |  | 1500 | 1.6 | 2.8 | 4.6 | 9.3 | 27.9 |  | 1500 | 2.6 | 4.4 | 7.4 | 14.7 | 44.2 | 
2000 | 2.3 | 3.9 | 6.5 | 13.0 | 38.9 |  | 2000 | 1.5 | 2.6 | 4.4 | 8.8 | 26.5 |  | 2000 | 2.4 | 4.2 | 7.0 | 14.0 | 41.9 | 
2500 | 2.2 | 3.7 | 6.2 | 12.4 | 37.3 |  | 2500 | 1.5 | 2.5 | 4.2 | 8.5 | 25.4 |  | 2500 | 2.3 | 4.0 | 6.7 | 13.4 | 40.2 | 
3000 | 2.1 | 3.6 | 6.0 | 12.0 | 36.0 |  | 3000 | 1.4 | 2.5 | 4.1 | 8.2 | 24.5 |  | 3000 | 2.2 | 3.9 | 6.5 | 12.9 | 38.7 | 
3500 | 2.0 | 3.5 | 5.8 | 11.6 | 34.8 |  | 3500 | 1.4 | 2.4 | 4.0 | 7.9 | 23.8 |  | 3500 | 2.2 | 3.8 | 6.3 | 12.5 | 37.5 | 
4000 | 2.0 | 3.4 | 5.6 | 11.3 | 33.9 |  | 4000 | 1.3 | 2.3 | 3.9 | 7.7 | 23.2 |  | 4000 | 2.1 | 3.6 | 6.1 | 12.2 | 36.5 | 
4500 | 1.9 | 3.3 | 5.5 | 11.0 | 33.0 |  | 4500 | 1.3 | 2.3 | 3.8 | 7.5 | 22.6 |  | 4500 | 2.1 | 3.6 | 5.9 | 11.8 | 35.5 | 
5280 | 1.8 | 3.2 | 5.3 | 10.6 | 31.8 |  | 5280 | 1.3 | 2.2 | 3.6 | 7.3 | 21.8 |  | 5280 | 2.0 | 3.4 | 5.7 | 11.4 | 34.3 | 

## Slide 62
TWDB Reported Well Yields Trinity Zones
ZONE 1
ZONE 3
ZONE 2

## Slide 63
Pumping Capacity of Well As Equipped (gpm) | Minimum Distance from Existing Water Well (ft)
ZONE 1 | 
Up to 17.36 gpm | 
> 17.36 to 30 gpm | 
> 30 gpm to 50 gpm | 
> 50 gpm to 100 gpm | 
> 100 gpm to 300 gpm | 
> 300 gpm | 
ZONE 2 | 
Up to 17.36 gpm | 
> 17.36 to 30 gpm | 
> 30 gpm to 50 gpm | 
> 50 gpm to 100 gpm | 
> 100 gpm to 300 gpm | 
> 300 gpm | 
ZONE 3 | 
Up to 17.36 gpm | 
> 17.36 to 30 gpm | 
> 30 gpm to 50 gpm | 
> 50 gpm to 100 gpm | 
> 100 gpm to 300 gpm | 
> 300 gpm | 

## Slide 64
Pumping Capacity of Well As Equipped (gpm) | Minimum Distance from Existing Water Well (ft)
ZONE 1 | 
Up to 17.36 gpm | 150
> 17.36 to 30 gpm | 150
> 30 gpm to 50 gpm | 150
> 50 gpm to 100 gpm | 1200
> 100 gpm to 300 gpm | na
> 300 gpm | na
ZONE 2 | 
Up to 17.36 gpm | 150
> 17.36 to 30 gpm | 150
> 30 gpm to 50 gpm | 150
> 50 gpm to 100 gpm | 500
> 100 gpm to 300 gpm | na
> 300 gpm | na
ZONE 3 | 
Up to 17.36 gpm | 150
> 17.36 to 30 gpm | 150
> 30 gpm to 50 gpm | 150
> 50 gpm to 100 gpm | 150
> 100 gpm to 300 gpm | 150
> 300 gpm | 150

## Slide 65
LIMITATIONS
Flowpaths are highly variable
GAM data are interpolated from sometimes limited data
Drawdowns are ESTIMATES and they represent pumping continuously for 50 years